## Slide 1: ECG FILTER DESIGN 26 MAY ,2021
VLSI PROJECT
Prof. Dr. Gaurav Trivedi
Associate Professor of Electronics and Electrical Engineering, IIT Guwahati
Ms. Meenali Janveja Research Scholar IIT Guwahati

## Slide 2: LITERATURE REVIEW
ECG FILTERS

## Slide 3: Recommendations for the Standardization and Interpretation of the Electrocardiogram
https://www.ahajournals.org/doi/pdf/10.1161/CIRCULATIONAHA.106.180200
https://www.scireslit.com/VascularMedicine/AJVM-ID18.pdf
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC3388307/

## Slide 4: Data set MIT-BIH Arrhythmia Database
https://www.physionet.org/content/mitdb/1.0.0/ The recordings were digitized at 360 samples per second per channel with 11-bit resolution over a 10 mV range. Two or more cardiologists independently annotated each record; disagreements were resolved to obtain the computer-readable reference annotations for each beat (approximately 110,000 annotations in all) included with the database.

## Slide 5: SPECIFICATION USED:
Stop band attenuation AS = 0db
Bandwidth = 0.5 - 40 Hz
Length of the filter N = 9
Sampling Frequency = 360 Hz
Pass band ripple Ap= = ?
Pass band edge frequency
stop band edge frequency

## Slide 6: FIR FILTER
All zero system (no pole)
Always stable
Easy to implement
Linear phase can be achieved =
Non recursive
Stable
No feedback
Group delay is min….. d( )/dw = -

## Slide 7: Linear phase FIR filter
TYPE 1
Symmetrical (
N= odd
h(n)=h(N-1-n) where N is the length of the filter
Best choise to design

## Slide 11: Kaiser window

## Slide 13: SPECIFICATION USED:
Stop band attenuation AS = 0db
Bandwidth = 0.5 - 40 Hz
Length of the filter N = 9
Order =N-1 =8
Sampling Frequency = 360 Hz

## Slide 14
FOLLOWING MATLAB SIMULATION OUTPUT USES
MIT-BIH Physionet 100.dat as dataset
https://physionet.org/content/mitdb/1.0.0/100.dat

## Slide 15: RECTANGULAR WINDOW

## Slide 17
h(n) =[ 0.0264 0.0961 0.1661 0.2177 0.2367 0.2177 0.1661 0.0961 0.0264]

## Slide 18
BARTLETT WINDOW

## Slide 20
h(n) =[0 0.0347 0.1198 0.2357 0.3416 0.2357 0.1198 0.0347 0]

## Slide 21
HAMMING WINDOW

## Slide 23
h(n) =[0.0028 0.0276 0.1200 0.2520 0.3167 0.2520 0.1200 0.0276 0.0028]

## Slide 24
HANNING WINDOW

## Slide 26
h(n) =[0.0031 0.0413 0.1351 0.2447 0.2941 0.2447 0.1351 0.0413 0.0031]

## Slide 27
BLACKMANN WINDOW

## Slide 29
h(n) =[0 0.0099 0.0876 0.2612 0.3671 0.2612 0.0876 0.0099 0]

## Slide 30
CHEBYCHEV WINDOW

## Slide 32
h(n) =[0.0027 0.0345 0.1260 0.2484 0.3078 0.2484 0.1260 0.0345 0.0027]

## Slide 33
KAISER WINDOW

## Slide 35
SHAPE PARAMETER (beta) = 4.5513
h(n) =[0.0019 0.0336 0.1266 0.2488 0.3072 0.2488 0.1266 0.0336 0.0019]

## Slide 36: Comparing windows
Now among different window function we select Kaiser window function for this application because its provides maximum stop band attenuation as compared to other window functions and also has a ripple control parameter and it is also more efficient in terms of the number of coefficients to meet the same specifications. Kaiser window is one of the useful and optimum window, optimum in sense of providing large main lobe width for the given stop-band attenuation which gives the sharpest transition width and it also provide flexible transition bandwidth.

## Slide 39: Direct form 1

## Slide 40
Direct form suffers delay , low performance however simple to design

## Slide 41: Direct form 2- pipelined

## Slide 42
Pipelined - Direct form II TRANSPOSED STRUCTURE

## Slide 43: Direct form 2 advantage than Direct form 1
Higher sampling rate
Delay is low

## Slide 44: Adders

## Slide 45: 4-bit Ripple carry adder

## Slide 46: 4-bit Carry select adder

## Slide 47: 4-bit carry look ahead adder

## Slide 48: 8- bit carry skip adder

## Slide 49: 8 – bit carry look ahead adder

## Slide 50: Carry select adder

## Slide 51: Adders
1. Ripple carry adder – cascade of FA – Slowest – n bit>>n full adders
Not efficient and high delay when bit size increases
2. Carry select adder – less delay (1/2 of ripple carry adder )
Faster & Less delay but mux occupy area . O(n
3. Carry look ahead adder – fastest in carry bypass logic in generating carry bits. As the no of bits increases , complexity increases as well as no of gates required for generating bypass logic increases>>more area and more power. The traditional CLA adder are not recommened to be designed as it consumes high power and more area, though fastest.
4. Carry skip adder – Carry bypass logic >>less delay than ripple carry adder

## Slide 52: Multipliers
Fastest – parallel multipliers like Wallace tree .
But Wallace suffers bad regularity and hard to design with high efficiency due to its complex layout.
So, when high performance ,lower power ,regularity is the primary concern , it is better to opt modified booth algo radix 4 or 8.
Modified Booth multiplier radix 4 on signed no’s in 2s complement .
No of partial products are reduced to n/2 in case of modified radix 4 booth multiplier.
In our case ,we will stick to radix 4 as no of bit we use is only 8 bits for signed multiplication.

## Slide 53: Memory occupancy
Booth multiplier has maximum number of ROMs, macros and BELS.
Wallace tree has minimum number of BELS and macros compared to Booth and Dadda multiplier.
Also,Wallace tree multiplier and Dadda multiplier have no flip-flops and Booth multiplier has maximum flip-flops.

## Slide 54: 8 X 8 bits Dadda and Wallace tree multipliers.
• Wallace tree multiplier uses 38 full adders and 15 half adders.
• Dadda multiplier uses 35 full adders and 7 half adders.
• Wallace tree multiplier requires a carry-propagate adder of 10 bits wide
• Dadda multiplier requires a carry propagate adder of 14 bits wide.
• The other disadvantage of Dadda multiplier is that it is less regular than the Wallace tree multiplier, making it more difficult to layout in VLSI design.
• Dadda multiplier has more number of intermediate stages. so, it has more number of interconnections (76.5% more).
• Both >> O(log(n))

## Slide 55: Objective: low power
Dadda multiplier consumes less area as compared to that of Wallace tree and Booth Multiplier.
Booth multiplier consumes less power as compared to that of Wallace tree and Dadda multiplier.
Wallace tree has less delay as compared to that of Booth and Dadda multipliers.

## Slide 57: FPGA vs ASIC Implementation

## Slide 58: Paper 1 : Design and Development of 8-Bits Fast Multiplier for Low Power Applications Vasudev G. and Rajendra Hegadi, Member, IACSIT

## Slide 59: Paper 1

## Slide 60: Wallace tree vs Daada

## Slide 61: Booth algorithm

## Slide 63: Booth algo:

## Slide 64: Ref: 3part 2 thesis

## Slide 66: Wallace tree

## Slide 67: MAC based FIR Filter: A novel approach for Low-Power Real-Time De-noising of ECG signals- paper Ramandeep Kaur¤, Rahul Malhotra†, Sujay Deb‡
The number of partial products are reduced to half by using Radix-4 Modified Booth Algorithm in comparison to Array and Vedic multiplier.

## Slide 68: Design and Implementation of Wallace Tree Multiplier using Higher Order Compressors DHANYA M RAVI
Ripple carry – cascade of FA , bit size increases, delay increases
Carry look ahead – carry for the next stages is calculated in advance based on input signals, Complexity increases with more than 4 bits >> hierarchial approach
Carry save adder – propagation delay is only 3 gates despite the no of bits . n FA used , the no of addition from 3 no’s to 2 no’s. The main application of carry save algorithm is, well known for multiplier architecture is used for efficient CMOS implementation of much wider variety of algorithms for high speed dsp.

## Slide 69: Carry save adder

## Slide 70: Wallace tree multiplier :
Advantages:
Compare to normal multiplication dalay is very low in Wallace multiplication.
Power consumption in the Wallace multiplier is low.
Speed is very fast i.e delay and power is inversely proposals to each other.
Disadvantages:
Memory occupation in Wallace tree multiplier is high, that is huge number of gates are used.

## Slide 72: Wallace multiplier with RCA Is implemented in the paper
Design and Implementation of Wallace Tree Multiplier using Higher Order Compressors DHANYA M RAVI